| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 05/11/02 |
| --- | --- | --- | --- | --- |
|  | IGT P/N | 69925300 | REV.NO | 0 |
|  |  |  | PAGE | 1/27 |

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 2/27 |

I N D E X

1. SAFETY PRECAUTIONS-------------------------------- 3

2. SPECIFICATIONS----------------------------------------- 4

3. TECHNICAL FEATURES ------------------------------- 5

4. TIMING CHART ------------------------------------------- 6

5. SET UP ------------------------------------------------------ 9

6. CONTROLS AND ADJUSTMENTS ------------------10

7. ADJUSTMENT SPECIFICATIONS------------------- 15

8. DESCRIPTION OF CIRCUIT OPERATION ------- 18

9. TROUBLE SHOOTING --------------------------------- 22

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 3/27 |

1. SAFETY PRECAUTIONS

WARNING: Service should not be attempted by anyone unfamiliar with the necessary precautions on this unit. The following precautions are necessary during servicing.

  - Some parts such as the picture tube in this unit have special safety-related characteristics for X-RAY RADIATION protection. For continued safety, parts replacement should be undertaken by referring to articles (1-2 ∼1-5).

  - Many electrical/mechanical parts in this unit have special safety-related characteristics for protection against electrical shock and other potential hazards. These characteristics often go unnoticed by a visual inspection and the protection afforded by them cannot necessarily be obtained by using replacement components rated for higher voltage, wattage, etc. Replacement parts, which have these special characteristics, are identified in the manual and highlighted on the schematic diagram and parts list. Before replacing these components read the parts list carefully.

  - When replacing chassis in the cabinet, always be certain that all the protective devices are installed properly, such as insulating covers, stain relief, etc.

  - Before replacing the back cover of the set, thoroughly inspect inside the cabinet to see that no stray parts or tools have been left inside.

1-5 Before returning the set to the customer always perform an ac leakage current check on the exposed metallic parts of the cabinet, such as terminal, screw heads, metal overlays, control shafts, etc. To be sure the set is safe to operate without danger of electrical shock, plug the AC power cable directly into a 115V AC outlet. (do not use a line isolation transformer during this check). Use an AC volt- meter with 5000 or more ohms per volt in the following manner. You cannot use a 1500 ohm, 10watt resistor, paralleled by a 0.15(uF) capacitor. Reverse the AC plug, the AC outlet and repeat the AC voltage measurements for each exposed metallic part. Voltage measured must not exceed 0.3V RMS.  This corresponds to 0.2mA AC. Any value exceeding this limit constitutes a potential shock hazard and must be corrected immediately.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 4/27 |

2. SPECIFICATIONS

2-1. Picture Tube

·Size : 19"

·Dot Pitch : 0.26mm

2-2. Signal Input

·Video Input : Analog, Positive Signal(0.7Vp-p)

·Horizontal Sync : TTL Level, Positive or Negative pulse.

·Scanning : 28Khz ∼ 70KHz

·Vertical Input : TTL Level, Positive or Negative pulse.

·Scanning : 40∼160Hz

2-3. Power Supply

·Power Input : AC100∼240V, 50/60Hz

·Fuse Rating : 250V, 50T 3.15A

·Power Consumption

Normal : less than 85W

DPMS  : less than 20W

2-4. External Control :

Refer to page 7.

2-5. Operating Temperature : 0℃∼55℃

2-6. Operating Humidity : 10%∼90%(Non-condensing)

2-7. Net weight  :  17kg

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 5/27 |

3. TECHNICAL FEATURES

3-1. U-com(MCU) control with OSD.

U-com recognizes the computer signal and signal output from control board connected with wire. So the circuit is simplified.

3-2. Universal AC input voltage.

Power supply operates on AC100∼265volt 50/60Hz for use all over the world.

3-3. Protection Circuit for over-current.

When over-current occurs in the circuit, the protection circuit operate in order to prevent the components from electrical shock or other risks.

3-4. Override function

The override function is designed for the normal display when the monitor is powered on without connection from the source (No signal message).

3-5. Control panel

If you are not satisfied with the factory mode size, position, color settings, use the control panel to program what you prefer in each resolution mode.

These adjusted settings are kept in memory even if you change resolution mode or turn off the monitor.

3-6. I2C BUS control

It is designed by I2C BUS control for simplifying circuit.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 6/27 |

4. TIMING CHART

Factory Pre-Set Timing Modes:

D

VIDEO

SYNC 		C			  E

A			B

| DESCRIPTION | MODE 1 VGA 720*400 | MODE 2 VGA 640*480 | MODE 3 8514/A 1024*768 | MODE 4 S-VGA 680*400 |
| --- | --- | --- | --- | --- |
| H | FH | 31.469KHz | 31.469KHz | 35.552KHz | 37.500KHz |
|  | A | 31.778㎲ | 31.778㎲ | 28.251㎲ | 26.667㎲ |
|  | B | 3.813㎲ | 3.813㎲ | 3.920㎲ | 2.032㎲ |
|  | C | 1.907㎲ | 1.589㎲ | 1.247㎲ | 3.810㎲ |
|  | D | 25.422㎲ | 25.422㎲ | 22.806㎲ | 20.317㎲ |
|  | E | 0.636㎲ | 0.318㎲ | 0.170㎲ | 0.508㎲ |
|  | POL. | NEGATIVE | NEGATIVE | POSITIVE | NEGATIVE |
| V | FH | 70.087Hz | 59.940Hz | 86.960KHz | 75.000Hz |
|  | A | 14.268ms | 16.683ms | 11.500ms | 13.333ms |
|  | B | 0.064ms | 0.064ms | 0.113ms | 0.080ms |
|  | C | 1.112ms | 0.794ms | 0.563ms | 0.427ms |
|  | D | 12.711ms | 15.253ms | 10.810ms | 12.800ms |
|  | E | 0.381ms | 0.064ms | 0.014ms | 0.027ms |
|  | POL. | POSITIVE | NEGATIVE | POSITIVE | NEGATIVE |
| VIDEO | ANALOG | ANALOG | ANALOG | ANALOG |

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 7/27 |
| DESCRIPTION | MODE5 S-VGA VESA 800*600 | MODE6 VGA 800*600 | MODE 7 VGA VESA 800*600 | MODE 8 VESA 1024*768 |
| H | FH | 37.879KHz | 46.875KHz | 48.077KHz | 48.363KHz |
|  | A | 26.400㎲ | 21.333㎲ | 20.800㎲ | 20.677㎲ |
|  | B | 3.200㎲ | 1.616㎲ | 2.400㎲ | 2.231㎲ |
|  | C | 2.200㎲ | 3.232㎲ | 1.280㎲ | 1.615㎲ |
|  | D | 20.000㎲ | 16.162㎲ | 16.000㎲ | 15.754㎲ |
|  | E | 1.000㎲ | 0.323㎲ | 1.119㎲ | 0.998㎲ |
|  | POL. | POSITIVE | POSITIVE | POSITIVE | NEGATIVE |
| V | FV | 60.317Hz | 75.000Hz | 72.188Hz | 60.004Hz |
|  | A | 16.579ms | 13.333ms | 13.853ms | 16.666ms |
|  | B | 0.106ms | 0.064ms | 0.125ms | 0.124ms |
|  | C | 0.607ms | 0.448ms | 0.478ms | 0.600ms |
|  | D | 15.840ms | 12.800ms | 12.480ms | 15.880ms |
|  | E | 0.026ms | 0.021ms | 0.772ms | 0.062ms |
|  | POL. | POSITIVE | POSITIVE | POSITIVE | NEGATIVE |
| VIDEO | ANALOG | ANALOG | ANALOG | ANALOG |

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 8/27 |

| DESCRIPTION | MODE 9 VESA 800*600 | MODE 10 VESA 1024*768 | MODE 11 VESA 1024*768 | MODE 12 VESA 1280*1024 | MODE 13 VESA 1024*768 |
| --- | --- | --- | --- | --- | --- |
| H | FH | 53.674KHz | 56.476KHz | 60.023KHz | 63.981KHz | 68.677KHz |
|  | A | 18.631㎲ | 17.707㎲ | 16.660㎲ | 15.698㎲ | 14.561㎲ |
|  | B | 1.138㎲ | 1.813㎲ | 1.219㎲ | 1.037㎲ | 1.016㎲ |
|  | C | 2.702㎲ | 1.920㎲ | 2.235㎲ | 2.296㎲ | 2.201㎲ |
|  | D | 14.222㎲ | 13.653㎲ | 13.003㎲ | 11.852㎲ | 10.836㎲ |
|  | E | 0.569㎲ | 0.321㎲ | 0.203㎲ | 0.360㎲ | 0.508㎲ |
|  | POL. | POSITIVE | NEGATIVE | POSITIVE | POSITIVE | POSITIVE |
| V | FV | 85.062Hz | 70.069Hz | 75.029Hz | 60.020Hz | 84.997Hz |
|  | A | 11.756ms | 14.272ms | 13.328ms | 16.638ms | 11.765ms |
|  | B | 0.056ms | 0.106ms | 0.050ms | 0.047ms | 0.044ms |
|  | C | 0.503ms | 0.513ms | 0.466ms | 0.594ms | 0.524ms |
|  | D | 11.179ms | 13.599ms | 12.795ms | 16.005ms | 11.183ms |
|  | E | 0.019ms | 0.054ms | 0.017ms | 0.016ms | 0.015ms |
|  | POL. | POSITIVE | NEGATIVE | POSITIVE | POSITIVE | POSITIVE |
| VIDEO | ANALOG | ANALOG | ANALOG | ANALOG | ANALOG |

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 9/27 |

5. SET UP

5-1. Start Up

Your monitor starts up automatically when you insert the power plug to power source.

AMP 25PIN							   MICROTOUCH

MICROTOUCH		DRAWER						     CONN.

CONTROLLER			   SENSOR GLASS

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 10/27 |

6. CONTROLS AND ADJUSTMENTS

There are four switches on the control panel.

Adjustable controls allow the best display status for individual preferences.

6-1. Key Function

① MODE

MODE - Call the Main-Menu OSD.

② SEL/DEGAUSS

SEL – Select the function (sub-Menu OSD) on the Main- Menu OSD.

DEGAUSS – Do degaussing if the OSD isn’t displayed.

③ DOWN/UP

-When the Main-Menu is displayed, you can search each function using these

keys.

-When the Sub-Menu is displayed(after select the function), can change

each state of the screen using these keys.

O.S.D Control

Sub-P.C.B

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 11/27 |

6.2. O.S.D CONTROL METHOD

- Control items.

| Location | Adjustment Method | Function |
| --- | --- | --- |
| SUB PCB | OSD Control | Brightness Contrast Horizontal Position Horizontal-Size Vertical Position Vertical-Size Side Pincushion Trapezoid Pin Balance Parallelogram |
| MAIN PCB | VR control VR301 VR501 VR502 VR503 FBT | H-MIN SIZE H.V Adjustment ABL Adjustment Sub-Bright Focus and Screen |

6-3. OSD Controls

- User’s control.

- BRIGHTNESS  ADJUSTMENT.

- Press the “MODE” key then Main-Menu OSD come out as below

Figure.

- Search “BRIGHTNESS” sub-menu by using the “UP/DOWN” key on the

Main-Menu OSD.

- Select the “BRIGHTNESS” by pressing the “SEL” key. Then the

“BRIGHTNESS” OSD color changes from yellow to red.

- Search the “BRIGHTNESS” sub-menu using the “UP/DOWN” key on the

Main-Menu OSD.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 12/27 |

- Select the “BRIGHTNESS” by pressing the “SEL” key. Then the

“BRIGHTNESS” OSD color changes from yellow to red.

- Adjust the Brightness as much as you want using the “UP/DOWN” key.

- After finishing the Brightness adjust, Press the “MODE” key then

the “BRIGHTNESS” OSD color changes from red to yellow and

be saved automatically.

- If you want to adjust other functions, search your sub-menu. For example, if you want to adjust the “CONTRAST” use the “UP/DOWN” keys and then adjust the same way as item 3),4) and 5).

To finish the adjustment press the “MODE” key then the OSD will disappear.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 13/27 |

| B. CONTRAST | ADJUST SAME WAY AS ABOVE |
| --- | --- |
| C. H. POSITION | ADJUST SAME WAY AS ABOVE |
| D. H. SIZE | ADJUST SAME WAY AS ABOVE |
| E. V. POSITION | ADJUST SAME WAY AS ABOVE |
| F. V. SIZE | ADJUST SAME WAY AS ABOVE |
| G. PINCUSHION | ADJUST SAME WAY AS ABOVE |
| H. TRAPEZOID | ADJUST SAME WAY AS ABOVE |
| I. PARALLELOG | ADJUST SAME WAY AS ABOVE |
| J. PIN BALANCE | ADJUST SAME WAY AS ABOVE |

K. COLOR ADJUSTMENT.

- Press the “MODE” key then the Main-Menu OSD come out as left

below figure.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 14/27 |

2) Press the “SELECT” key to adjust the “RED”,”GREEN” and “BLUE”

The “RED”,”GREEN” and “BLUE” is selected by pressing the

“SELECT” key and selected item change the OSD color from white to it’s

own color as character (ex: “RED” goes to red color)

3) Adjust the “RED”,”GREEN” or “BLUE” by using teh “UP/DOWN” key.

4) Press the “MODE” key to finish the color adjustment then the OSD goes

back to Main-Menu.

5) Press the “MODE” key again to finish the adjustment then the OSD

disappears.

L. RECALL.

When you press the “RECALL” key, all user’s adjustment values are erased

and covered by factory adjustment value.

At first stage without any user adjustments, The monitor is set up by

the factory adjustment value.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 15/27 |

7. Adjustment Specifications

7-1. Adjustment Sequence.

You should allow15minutes for the unit to warm up before adjustmenting.

7-2. Adjustment Sequence.

FBT High Voltage → G2 Voltage → Raster. Center → Hor. Size → Hor. Position → Ver. Size → Ver. position → Side-pin → Trapezoid → Focus → White balance → Convergence

7-3. Adjustment Procedure.

How to enter the Factory Mode : Press SEL and UP key simultaneously.

7-3.1. H/V voltage adjustment.

1) Input the cross-hatch pattern with the 31KHz 640*480 mode.

- After connecting a HIGH voltage meter to the ANODE, adjust the

VR 501 to 27kv.

7-3.2. G2 Voltage adjustment.

1) Input the cross-hatch pattern with 31KHz 640*480 mode

2) After connecting a DC high voltage meter to the G2 of the CRT socket, adjust G2 voltage to 560V ± 10V by changing SCREEN  VR of FBT.

7-3.3 G/D Adjustment.

Refer to controls and adjustment.(Article 6)

7-3.4 Focus adjustment.

1) Input the "H" character pattern with 60KHz 1024*768 .

2) Adjust the focus for the best balance at each point of A, B, C, D, E as shown below by rotating the focus VR of FBT.

| 3/4 |  | A |  |  |  | B |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2/4 |  |  |  | E |  |  |  |
| 1/4 |  | D |  |  |  | C |  |
|  |  | 1/4 |  | 2/4 |  | 3/4 |  |

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 16/27 |

7-3.5. White balance Adjustment.

Pre-adjustment

1) This should be carried out at least 15 minutes.

2) Input the window pattern with 53KHz 800*600 mode.

3) Degauss the screen with Manual degaussing coil.

White Balance adjustment(Back Raster)

1) Remove the video signal

2) Adjust the sub-brightness of back raster to be 0.35±0.05FT/L with R,G,B BIAS

3) And, adjust the color temperature to be X=0.281 ±0.02 and Y= 0.311 ±0.02 by R.G.B bias control function on OSD menu.

4) Adjust BRIGHTNESS to be 0.35FL ±0.05 F/L.

White Balance adjustment(Video)

1) Input the 20% window pattern with 53KHz 800*600mode.

2) Adjust the color temperature to be X=0.281 ±0.015 and Y=0.311 ±0.02 by R.B gain on OSD menu.

3) Adjust CONTRAST to be 66FL ±5 F/L.

7-3.6. Purity and Convergence Adjustment.

1) Purity Adjustment.

①Demagnetize the picture tube and cabinet using a degaussing coil.

②Turn the CONTRAST and BRIGHTNESS controls to maximum.

③Adjust RED and BLUE bias controls to provide only a green raster

④Loosen the clamp screw holding the yoke, and slide the yoke, backward to provide vertical green belt(zone) in the picture screen.

⑤Remote the Rubber wedges.

⑥Rotate and spread the tabs of the purity magnet see figure 1 around the neck of the picture tube until the green belt is in the center of the screen. At the same time, center the raster vertically.

⑦Move the yoke forward slowly until a uniform green screen is obtained. Tighten the clamp screw of the yoke temporarily.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 17/27 |

⑧Check the purity of the red and blue raster by adjusting the bias controls.

⑨Obtain a while raster, referring to CRT GRAY SCALE ADJUSTMENT

⑩Proceed with convergence adjustment.

2) Convergence adjustment.

①.Receive crosshatch pattern with a color bar signal generator.

②.Adjust the BRIGHTNESS and CONTRAST controls for a well defined pattern.

③.Adjust two tabs of the 4-Pole Magnets to change the angle between them(See figure 1) and superimpose the red and blue vertical lines in the center area of the picture screen.

④.Turn both tabs at the same time keeping their angles constant to superimpose the red and blue horizontal lines at the center of the screen.(See figure 2.)

⑤.Adjust two tabs of 6-Pole Magnets to superimpose red/blue line with green one. Adjusting the angle affects the vertical lines and rotating both magnets affects the horizontal lines

⑥.Repeat adjustment ③, ④ and ⑤. Keeping in mind red, green and blue movement, because 4-Pole Magnets and 6-Pole Magnets are interacted and make dot movement complex.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 18/27 |

8. DESCRIPTION OF CIRCUIT OPERATION

8-1. Mode control

8-1.1. H-Sync is inputted to pin 31 of IC601, V-Sync to pin 30 of IC601 for each mode, and pin 28, 29 of IC601 output always positive polarity sync.

8-1.2. The outputs from IC601 are as below(See Table 1)

| No. | Frequency | Resolution | Range of Frequency | OUT PUT (MCU PIN) |
| --- | --- | --- | --- | --- |
|  | Hf kHz | Vf Hz |  | Hf (kHz) | Vf (Hz) | CS2 39 | CS1 40 | CS0 41 | SUS- 4 |
| 1 | 31 | 70 | 720x400 | 28∼32.9 | 68∼72 | L | L | L | H |
| 2 | 31 | 60 | 640x480 | " | 58∼62 | L | L | L | H |
| 3 | 35 | 86 | 1024x768 | 33∼35.9 | 84∼88 | H | L | L | H |
| 4 | 38 | 75 | 640x480 | 36∼40.9 | 73∼77 | L | H | L | H |
| 5 | 38 | 60 | 800x600 | 36∼40.9 | 58∼62 | L | H | L | H |
| 6 | 47 | 75 | 800x600 | 41∼51.9 | 73∼77 | H | L | H | H |
| 7 | 48 | 72 | 800x600 | " | 70∼74 | H | L | H | H |
| 8 | 48 | 60 | 1024x768 | " | 58∼62 | H | L | H | H |
| 9 | 53 | 85 | 800x600 | 52∼61.9 | 83∼87 | L | H | H | H |
| 10 | 56 | 70 | 1024x768 | " | 68∼72 | L | H | H | H |
| 11 | 60 | 75 | 1024x768 | " | 73∼77 | L | H | H | H |
| 12 | 64 | 60 | 1280x1024 | 62∼70 | 58∼62 | H | H | H | H |
| 13 | 69 | 85 | 1024x768 | 62∼70 | 83∼87 | H | H | H | H |
| 14 | - | - | - | H≤10 | NORMAL | X | X | X | L |
| 15 | - | - | - | NORMAL | V≤40 | X | X | X | L |
| 16 | - | - | - | H≤10 | V≤40 | X | X | X | L |
| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 19/27 |

8-2. Deflection Processor (IC301)

8-2.1. Horizontal section

1) Horizontal oscillation

R314 and C347 set horizontal free frequency .

Auto-sync processing can be done from 30KHz to 70KHz by mean of IC301 without any adjustment.

2) Phase shift

Horizontal phase shift is controlled by IC601 using I2C BUS control.

3) Horizontal driver output

The output pulse, which has the duty-cycle of 47%, is available at pin 26 of IC301.

This output is used for horizontal drive circuit.

4) B+ control driver output

The output pulse is available at pin 28 of IC301 and it is used for

H-scan voltage control driver.

5) X-ray protection

When the fly-back voltage rises up to unacceptable level X-ray protection is activated X-ray input pin 36 of ic601 is above 3.2v

This result is that complete line drive stage stops working.

The reset of this protection is obtained by Main power off.

8-2.2. Vertical section

1) Vertical oscillation

The free running frequency of the vertical oscillator is determined by the capacitor C342 at pin VCAP(pin22) of IC301.

2) Vertical amplitude

Vertical amplitude is controlled by IC601 using I2C.

3) Vertical position

Vertical position is controlled by IC601 using I2C.

4) Ease-west parabola

A parabola waveform is available on pin 24 of IC301 for driving the pincushion correction stage. Amplitude of parabola waveform is controlled by IC601 using I2C.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 20/27 |

8-2.3. B+ Regulator

B+ PWM regulator output is available on pin 28 of IC301 for driving the B+ control stage.

8-3. Vertical Deflection (IC201)

IC201 (KA2142) is used for direct driving of vertical deflection yoke.

8-4. Horizontal scan voltage control stage

The step-up converter is used in this stage.

The output pulse at pin 28 of the IC301 is synchronized on horizontal frequency. And this pulse is operated via buffer stage Q353,Q354

This output is rectified through D308,C328.

8-5. Horizontal deflection output stage

8-5.1. Line driver stage

As a driver device, small TR Q305(C3502E) is used.

The driver transformer T302 is equipped with a snubber circuit (R327/C309) at the primary side to damp excessive ringing.

8-5.2. Horizontal power output stage

The horizontal power output stage is used boost-up circuit.

As a deflection transistor, the Q308(J6825) is used.

To compensate the horizontal linearity, T301 is connected in a series

with the horizontal DY. It is controlled by DC collector voltage of Q304,

which the base voltage of Q304 is integrated from output at pin 24 of

IC601.

8-5.3. S-correction capacitor switches

Q316 is off when horizontal frequency is 35KHz.

Q317 is off when horizontal frequency is 37KHz.

Q316,Q318 is off when horizontal frequency is 44KHz~52KHz.

Q317,318 is off when horizontal frequency is 53KHz∼61KHz.

Q316,Q317,Q318 is off when horizontal frequency is 62KHz∼70KHz.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 21/27 |

8-6. FBT(Fly-back Transformer)

As a driver device, IC302(KA7500) is used.

The high voltage for CRT anode ,focus, G2 voltage for CRT and 800V for FOCUS VOLTAGE are generated by the FBT.

Also, -130V for G1 voltage, 26V for X-RAY detect voltage are extracted from the FBT.

In this way, the supply voltage to the fly-back transformer can be proportional to the horizontal line frequency.

8-7. . ABL(Automatic Beam Limiting)

The voltage of the FBT pin10 is affected by the anode current of the FBT.

When the voltage at pin 10 is decreased, the anode current is increased accordingly. When the current anode is increased, contrast is set at the certain limited level (28FL in white pattern) that is set by inner voltage of IC401.

8-8. Video amplification section.

8-8.1. Video pre-amplifier (IC401)

Input video signals are amplified by means of IC401, and the amplified signals drive the video output stage(IC402).

Video gain is adjusted by DC voltage at pin 12 for ABL control.

8-8.2. Video output stage (IC402)

The video output signal from IC401 is amplified again by IC402, and IC402 apply video signal to each cathode of CRT.

Q405, Q406 and Q407, which is operated by I2C BUS control through u-com, adjust cutoff voltages.

8-8.3. OSD(On Screen Display : IC403)

The OSD signal is applied from IC403 to IC402.

It is controlled by I2C BUS control line.

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 22/27 |

9. TROUBLE SHOOTING

9-1. NO POWER

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 23/27 |

9-2. NO VIDEO

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 24/27 |

9-3. NO RASTER

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 25/27 |

9-4. TROUBLE IN HORIZONTAL SIZE

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 26/27 |

9-5. TROUBLE IN CONTRAST

| TOVIS | TOVIS P/N | MTG-1902MM | DATE | 2002.05.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV.NO | 0 |
|  |  |  | PAGE | 27/27 |

9-6. TROUBLE IN BRIGHTNESS

# Text boxes

CHECK & REPLACEMENT

Q353,354

min->1-99->max

CHECK & REPLACEMENT

IC301

YES

NO

CHECK IC301

#28 WAVEFORM

NO

YES

CHECK & REPLACEMENT

Q308,D308

YES

NO

POWER CIRCUIT

CHECK 45V

CHECK Q352

DRAIN

WAVEFORM

H-SIZE

CHECK & REPLACEMENT

IC401

YES

CHECK & REPLACEMENT

IC601

NO

CHECK IC401

#18 WAVEFORM

YES

CHECK & REPLACEMENT

IC401

CHECK IC401

#12 VOLTAGE

CHECK & REPLACEMENT

Q507

YES

CHECK POWER BOARD

NO

CHECK

HT LINE

YES

NO

CONTRAST

CHECK & REPLACEMENT

D318

NO

CHECK

G1 VOLTAGE

BRIGHTNESS

Color Monitor Service Manual

MODEL: MTG – 1902MM

CHECK C112

AC LEVEL

NO POWER

NO

CHECK&

REPLACEMENT

F101, POWER CORD

YES

NO

CHECK C114

DC LEVEL

CHECK & REPLACEMENT

BD101

YES

NO

CHECK IC105

#7 WAVEFORM

CHECK & REPLACEMENT

IC105

YES

CHECK IC101

#3 WAVEFORM

NO

CHECK & REPLACEMENT

IC101

YES

CHECK &

REPLACEMENT

SECONDARY VOLTAGE OF T101

NO VIDEO

CHECK

SIGNAL CABLE

NO

CHECK&

REPLACEMENT

SIGNAL CABLE

YES

CHECK IC401

#21,24,26 PULSE

NO

CHECK IC401

#23 DC LEVEL &

#18,19 PULSE

YES

NO

CHECK&

REPLACEMENT

IC601,Q204

YES

CHECK&

REPLACEMENT

IC401

CHECK IC402

#1,3,5 PULSE

NO

CHECK&

REPLACEMENT

IC402

YES

CHECK&

REPLACEMENT

CRT SOCKET, G1

NO RASTER

CHECK

HV & G2

NO

YES

CHECK Q319

WAVEFORM

YES

CHECK

G1 & DC 80V

CHECK & REPLACEMENT

FBT,CRT

YES

NO

CHECK Q319

BASE

NO

YES

CHECK & REPLACEMENT

Q507

NO

CHECK & REPLACEMENT

Q313,Q311,D312

CHECK & REPLACEMENT

Q307,Q309,Q310