| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 03/11/02 |
| --- | --- | --- | --- | --- |
|  | IGT P/N | 69925100 | REV NO. | 0 |
|  |  |  | PAGE | 1/30 |

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 2/30 |

I N D E X

1. SAFETY PRECAUTIONS ------------------------------- 3

2. SPECIFICATIONS ---------------------------------------- 4

3. TECHNICAL FEATURES ------------------------------- 5

4. TIMING CHART ------------------------------------------- 6

5. SET UP ------------------------------------------------------ 8

6. CONTROLS AND ADJUSTMENTS ------------------ 9

7. ADJUSTMENT SPECIFICATION -------------------- 18

8. DESCRIPTION OF CIRCUIT OPERATION ------- 21

9. TROUBLE SHOOTING --------------------------------- 25

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 3/30 |

1. SAFETY PRECAUTIONS

WARNING: Service should not be attempted by anyone unfamiliar with the necessary precautions on this unit. The following precautions are necessary during servicing.

  - Some parts such as a picture tube in this unit have special safety-related

Characteristics for X-RAY RADIATION protect.

For continued safety, the parts replacement should be under taken referring to

below article(1-2 ∼ 1-5).

  - Many electrical mechanical parts in this unit have special safety-related characteristics for protection against shock hazard and others.

These characteristics are often passed unnoticed by a visual inspection and the protection afforded by them cannot necessarily be obtained by using replacement components rated for higher voltage wattage, etc.

Replacement parts, which have these special characteristics, are identified in the manual and supplements by shading on the schematic diagram and the parts list. Before replacing these components read the parts list in this manual carefully.

  - When replacing the chassis in the cabinet, always be certain that all the protective devices are installed properly, such as insulating covers, stain relief, etc.

  - Before replacing the back cover of the set, thoroughly inspect inside the cabinet to see that no stray parts or tools have been left inside.

1-5 Before returning the set to the customer always perform an ac leakage current check on the exposed metallic parts of the cabinet, such as terminal, screw heads, metal overlays, control shafts, etc. To be sure the set is safe to operate without danger of electrical shock, plug the AC line cord directly into a 115V AC outlet (do not use a line isolation transformer during this check). Use an AC volt- meter having 5000 ohms per volt or more sensitivity in the following manner. Cannot use a 1500 ohm, 10watt resistor, paralleled by a 0.15(uF) capacitor. Reverse the AC plug in the AC outlet and repeat AC voltage measurements for each exposed metallic part. Voltage measured must not exceed 0.3V RMS.  This corresponds to 0.2mA AC any value exceeding this limit constitutes a potential shock hazard and must be corrected immediately.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 4/30 |

2. SPECIFICATIONS

2-1. Picture Tube

·Size : 19"

·Dot Pitch : 0.25mm

2-2. Signal Input

·Video Input : Analog, Positive Signal(0.7Vp-p)

·Horizontal Sync : TTL Level, Positive or Negative pulse.

·Scanning : 28Khz ∼ 70KHz

·Vertical Input : TTL Level, Positive or Negative pulse.

·Scanning : 40∼160Hz

2-3. Power Supply

·Power Input : AC100∼240V, 60/50Hz

·Fuse Rating : 250V, 50T 3.15A

·Power Consumption

Normal: less than 130W

DPMS: less than 20W

2-4. External Control:

Refer to page 7.

2-5. Operating Temperature: 0℃∼55℃

2-6. Operating Humidity: 10%∼90%(Non-condensing)

2-7. Net weight:  23kg

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 5/30 |

3. TECHNICAL FEATURES.

3-1. U-com(MCU) control with OSD.

U-com recognizes the computer signal and the signal output from control board connected with wire. So the circuit is simplified.

3-2. Universal AC input voltage.

Power supply operates on AC100∼240volt 60/50Hz for use all over the world.

3-3. Protection Circuit for over-current.

When over-current happens in the circuit, the protection circuit operates in order to prevent the components from electrical shock or other risks.

3-4. Override function

Is designed for the normal display when the monitor is powered on without connection from the source (No signal message).

3-5. Control panel

If you are not satisfied with the factory mode size, position, color settings, use the control panel to program those you prefer in each resolution mode.

Then, these adjusted settings are kept in memory even if you change resolution mode or turn off the monitor.

3-6. I2C BUS control

It is designed by I2C BUS control for simplifying the circuit. The number of total components is less than 610 pcs.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 6/30 |

4. TIMING CHART

Factory Pre-Set Timing Modes.

D

VIDEO

C                     E

SYNC

B

A

| DESCRIPTION | MODE 1 VGA 720*400 | MODE 2 VGA 640*480 | MODE 3 8514/A 1024*768 | MODE 4 S-VGA 680*400 |
| --- | --- | --- | --- | --- |
| H | FH | 31.469KHz | 31.469KHz | 35.552KHz | 37.500KHz |
|  | A | 31.778㎲ | 31.778㎲ | 28.251㎲ | 26.667㎲ |
|  | B | 3.813㎲ | 3.813㎲ | 3.920㎲ | 2.032㎲ |
|  | C | 1.907㎲ | 1.589㎲ | 1.247㎲ | 3.810㎲ |
|  | D | 25.422㎲ | 25.422㎲ | 22.806㎲ | 20.317㎲ |
|  | E | 0.636㎲ | 0.318㎲ | 0.170㎲ | 0.508㎲ |
|  | POL. | NEGATIVE | NEGATIVE | POSITIVE | NEGATIVE |
| V | FH | 70.087Hz | 59.940Hz | 86.960KHz | 75.000Hz |
|  | A | 14.268ms | 16.683ms | 11.500ms | 13.333ms |
|  | B | 0.064ms | 0.064ms | 0.113ms | 0.080ms |
|  | C | 1.112ms | 0.794ms | 0.563ms | 0.427ms |
|  | D | 12.711ms | 15.253ms | 10.810ms | 12.800ms |
|  | E | 0.381ms | 0.064ms | 0.014ms | 0.027ms |
|  | POL. | POSITIVE | NEGATIVE | POSITIVE | NEGATIVE |
| VIDEO | ANALOG | ANALOG | ANALOG | ANALOG |

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 7/30 |

| DESCRIPTION | MODE5 S-VGA VESA 800*600 | MODE6 VGA 800*600 | MODE 7 VGA VESA 800*600 | MODE 8 VESA 1024*768 |
| --- | --- | --- | --- | --- |
| H | FH | 37.879KHz | 46.875KHz | 48.077KHz | 48.363KHz |
|  | A | 26.400㎲ | 21.333㎲ | 20.800㎲ | 20.677㎲ |
|  | B | 3.200㎲ | 1.616㎲ | 2.400㎲ | 2.231㎲ |
|  | C | 2.200㎲ | 3.232㎲ | 1.280㎲ | 1.615㎲ |
|  | D | 20.000㎲ | 16.162㎲ | 16.000㎲ | 15.754㎲ |
|  | E | 1.000㎲ | 0.323㎲ | 1.119㎲ | 0.998㎲ |
|  | POL. | POSITIVE | POSITIVE | POSITIVE | NEGATIVE |
| V | FV | 60.317Hz | 75.000Hz | 72.188Hz | 60.004Hz |
|  | A | 16.579ms | 13.333ms | 13.853ms | 16.666ms |
|  | B | 0.106ms | 0.064ms | 0.125ms | 0.124ms |
|  | C | 0.607ms | 0.448ms | 0.478ms | 0.600ms |
|  | D | 15.840ms | 12.800ms | 12.480ms | 15.880ms |
|  | E | 0.026ms | 0.021ms | 0.772ms | 0.062ms |
|  | POL. | POSITIVE | POSITIVE | POSITIVE | NEGATIVE |
| VIDEO | ANALOG | ANALOG | ANALOG | ANALOG |

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 8/30 |

| DESCRIPTION | MODE 9 VESA 800*600 | MODE 10 VESA 1024*768 | MODE 11 VESA 1024*768 | MODE 12 VESA 1280*1024 | MODE 13 VESA 1024*768 |
| --- | --- | --- | --- | --- | --- |
| H | FH | 53.674KHz | 56.476KHz | 60.023KHz | 63.981KHz | 68.677KHz |
|  | A | 18.631㎲ | 17.707㎲ | 16.660㎲ | 15.698㎲ | 14.561㎲ |
|  | B | 1.138㎲ | 1.813㎲ | 1.219㎲ | 1.037㎲ | 1.016㎲ |
|  | C | 2.702㎲ | 1.920㎲ | 2.235㎲ | 2.296㎲ | 2.201㎲ |
|  | D | 14.222㎲ | 13.653㎲ | 13.003㎲ | 11.852㎲ | 10.836㎲ |
|  | E | 0.569㎲ | 0.321㎲ | 0.203㎲ | 0.360㎲ | 0.508㎲ |
|  | POL. | POSITIVE | NEGATIVE | POSITIVE | POSITIVE | POSITIVE |
| V | FV | 85.062Hz | 70.069Hz | 75.029Hz | 60.020Hz | 84.997Hz |
|  | A | 11.756ms | 14.272ms | 13.328ms | 16.638ms | 11.765ms |
|  | B | 0.056ms | 0.106ms | 0.050ms | 0.047ms | 0.044ms |
|  | C | 0.503ms | 0.513ms | 0.466ms | 0.594ms | 0.524ms |
|  | D | 11.179ms | 13.599ms | 12.795ms | 16.005ms | 11.183ms |
|  | E | 0.019ms | 0.054ms | 0.017ms | 0.016ms | 0.015ms |
|  | POL. | POSITIVE | NEGATIVE | POSITIVE | POSITIVE | POSITIVE |
| VIDEO | ANALOG | ANALOG | ANALOG | ANALOG | ANALOG |

5. SET UP

Setting up your monitor is easy. All you have to do is make a few simple connections and adjustments. The procedure is as follows.

5-1. Start Up

Your monitor starts up automatically when you insert the power plug to power source.

5-2. Signal cable Connection

Connect the 15pin-signal cable to the source. And Lock both screws to ensure that the monitor is properly grounded.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 9/30 |

AMP 19pin connector

| NO. | DESCRIPTION | NO. | DESCRIPTION |
| --- | --- | --- | --- |
| 1 |  | 11 | TOUCH_RxD |
| 2 | VIDEO RED | 12 | NET GND |
| 3 | VIDEO BLUE | 13 | AC GND |
| 4 | VIDEO GREEN | 14 | AC2 |
| 5 | HOR-SYNC | 15 | AC1 |
| 6 | VER-SYNC | 16 | A GND |
| 7 | VIDEO GND | 17 | +13V DC(A) |
| 8 |  | 18 | AC2 |
| 9 | TOUCH_TxD | 19 | AC1 |
| 10 |  |  |  |

6. CONTROLS AND ADJUSTMENTS

There are four switches on the control panel.

Adjustable controls allow the best display status for individual preferences.

6-1. Key Function

① MODE

MODE - Call the Main-Menu OSD.

② SEL/DEGAUSS

SEL – Select the function (sub-Menu OSD) on the Main- Menu OSD.

DEGAUSS – Do degaussing in state that the OSD isn’t displayed.

③ DOWN/UP

-When the Main-Menu is displayed, can search each function using these

Keys.

-When the Sub-Menu is displayed (after select the function), can change

each state of the screen using these keys.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 10/30 |

O.S.D Control Sub-P.C.B

6.2. O.S.D CONTROL METHOD

1) Control items.

| Location | Adjustment Method | Function |
| --- | --- | --- |
| SUB PCB | OSD Control | Brightness Contrast Horizontal Position Horizontal-Size Vertical Position Vertical-Size Side Pincushion Trapezoid Pin Balance Parallelogram |
| MAIN PCB | VR control, VR501 VR301 FBT | Sub-Bright H.V Adjustment Focus and Screen |

6-3. OSD Controls

- User’s control.

- BRIGHTNESS ADJUSTMENT.

- Press the “MODE” key then Main-Menu OSD come out as below

Figure.

- Search “BRIGHTNESS” sub-menu using “UP/DOWN” key on the

Main-Menu OSD.

- Select the “BRIGHTNESS” by pressing “SEL” key. Then The

“BRIGHTNESS” OSD color changes from yellow to red.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 11/30 |

- Adjust Brightness as much as you want using “UP/DOWN” key.

- After finishing the Brightness adjustment, Press the “MODE” key then

The “BRIGHTNESS” OSD color changes from red to yellow and the

changed brightness value is saved automatically.

- If you want to adjust other functions (sub-menu), Search your Sub-menu example: “CONTRAST” using “UP/DOWN” keys and then adjust the same

way as item 3),4) and 5).

- Press the “MODE” key again to finish the adjustment then the OSD menu will disappear.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 12/30 |

| B. CONTRAST | ADJUST SAME WAY AS ABOVE |
| --- | --- |
| C. H. POSITION | ADJUST SAME WAY AS ABOVE |
| D. H. SIZE | ADJUST SAME WAY AS ABOVE |
| E. V. POSITION | ADJUST SAME WAY AS ABOVE |
| F. V. SIZE | ADJUST SAME WAY AS ABOVE |
| G. PINCUSHION | ADJUST SAME WAY AS ABOVE |
| H. TRAPEZOID | ADJUST SAME WAY AS ABOVE |
| I. PARALLELOG | ADJUST SAME WAY AS ABOVE |
| J. PIN BALANCE | ADJUST SAME WAY AS ABOVE |

K. COLOR ADJUSTMENT.

- Press the “MODE” key then Main-Menu OSD come out as left

below figure.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 13/30 |

2) Search “COLOR” sub-menu using “UP/DOWN” key on the

Main-Menu OSD.

3) Select the “COLOR” by pressing “SEL” key. Then the color Sub-Menu OSD comes out as right below figure.

- 4) Search “USER” using “UP/DOWN” key (“COLOR1” and “COLOR2”

- is adjusted in factory by an auto-alignment machine. )

5) Press “SELECT” key to adjust “RED”,”GREEN” and “BLUE”

“RED”,”GREEN” and “BLUE” is selected by pressing the

“SELECT” key and selected item changes OSD color from white to it’s

corresponding color (ex: “RED” goes to red color)

- ) Adjust “RED”,”GREEN” or “BLUE” using “UP/DOWN” key.

7) Press “MODE” key to finish the color adjustment then the OSD goes

back to Main-Menu.

8) Press the “MODE” key again to finish the adjustment then the OSD will

disappear.

L. RECALL.

When the “RECALL” key is selected adjusted values are erased

and replaced by the factory adjustment values.

At first without any user’s adjustment, the monitor has a factory set up.

M. LANGUAGE.

There are 4 languages provided for ease of use.

(Factory setting is English)

- Press the “MODE” key then Main-Menu OSD comes up.

- Search “LANGUAGE” sub-menu using “UP/DOWN” key on the

Main-Menu OSD.

- Select the “LANGUAGE” by pressing “SEL” key. Then The

Language sub-menu comes up as below figure.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 14/30 |

4) Search any language using “UP/DOWN” key.

5) Select a language by pressing the “SEL” key.

6) Press “MODE” key to finish and save the selected language.

Then the OSD return to Main-Menu in selected language.

7) Press the “MODE” key again to finish the adjustment then the OSD will

disappear.

LANGUAGE

ENGLISH

FRANCAIS

ESPANOL

PORTUGUES

- Factory control.

This monitor has two-adjustment modes.

One is for the user’s own adjustments and other is for factory adjustments only.

Factory adjustments may be required during repair.  Incorrect factory adjustments may adversely affect the user adjustment mode.  Any factory adjustment errors can be recovered using the “RECALL” function (refer to 6-3 M item)

A. Factory mode entering.

Press the “MODE” and “DOWN” key simultaneously until OSD comes

out as below.

The OSD of factory mode is same format as the user mode except the color

of the bottom line. (User mode is blue; factory mode is red as shown below)

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 15/30 |

B. Exit and save.

- After finishing the adjustment; search “RECALL” using the “UP/DOWN” key.

- Press the “SEL” key until the OSD disappears then the adjusted value is saved.  Exit from the factory mode.

C. Adjustment.

All adjustment methods are the same as the user’s control mode except “COLOR”.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 16/30 |

D.COLOR ADJUSTMENT.

- Before adjusting  “COLOR”, “CONTRAST” and “BRIGHTNESS” fix levels at

maximum. (It’s a TOVIS’s reference condition.)

- At the factory mode, search “COLOR” using “UP/DOWN” key.

- Select “COLOR” by pressing “SEL” key then the color sub-menu comes up

as in figure below left.

- Search a color temperature that you want to adjust (gain or bias)

using “UP/DOWN” key.

( “GAIN” means high-beam area’s adjustment and “BIAS” means

low-beam area’s adjustment.)

- Select any item wanted by pressing “SEL” key then the OSD

changes to under sub-menu as right below figure.

- Adjust color temperature using “UP/DOWN” and “SEL” key.

( “UP/DOWN” key: moves item position, “SEL” key : changes value.)

- At the “GAIN” mode, “CO” means sub-contrast adjustment.

Sub-contrast can be adjusted using “UP/DOWN” key if necessary.

(To meet the white peak “ft” level.)

- Press “MODE” key to finish the “GAIN” or “BIAS” adjustment.

- If you want to adjust other “GAIN” or “BIAS”,

Repeat from item 4) to 8).

- Press “MODE” key to finish the “COLOR” adjustment.

- If you want to finish factory adjustment, Select “RECALL”

as in item “B. Exit and save”

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 17/30 |

9300 GAIN   9300 BIAS

6500 GAIN   6500 BIAS

At           RG       GG

GAIN        BG       CO

OR

At           RB        GB

BIAS.        BB

“SEL” and “UP/DOWN”

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 18/30 |

7. Adjustment Specification

7-1.  Adjustment Sequence.

It needs minimum of 15 minutes of warm up time before adjustment.

7-2.  Adjustment Sequence.

FBT B+ Voltage → G2 Voltage → Hor. Center → Hor. Size → Hor. Position → Ver. Size → Ver. position → Side-pin → Trapezoid → Focus → White balance → Convergence

7-3.  Adjustment Procedure.

How to enter the Factory Mode : Press Menu and Down key simultaneously.

7-3. 1. FBT B + voltage adjustment.

1) Input the crosshatch pattern with the 48KHz 1024*768 mode.

2) After connecting a digital voltage meter to the each pin of D316, anode and cathode adjust FBT B+ voltage to 114V ± 1.0V using VR301.

7-3. 2. G2 Voltage adjustment.

1) Input the cross-hatch pattern with 48KHz 1024*768 mode

2) After connecting a DC high voltage meter to the G2 of the CRT socket, adjust G2 voltage to 600V ± 10V by changing SCREEN  VR of FBT.

7-3. 3  G/D Adjustment.

Refer to controls and adjustment.(Article 6)

7-3. 4  Focus adjustment.

1) Input the "H" character pattern with 48KHz 1024*768 .

2) Adjust the focus for the best balance at each point of A, B, C, D, E as shown below by rotating the focus VR of FBT.

| 3/4 |  | A |  |  |  | B |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2/4 |  |  |  | E |  |  |  |
| 1/4 |  | D |  |  |  | C |  |
|  |  | 1/4 |  | 2/4 |  | 3/4 |  |

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 19/30 |

7-3.5. White balance Adjustment. (25% Window Box pattern)

Pre-adjustment

1) This should be carried out for at least 15 minutes.

2) Input the window pattern with 31KHz 640*480 mode.

3) Degauss the screen with Manual degaussing coil.

White Balance adjustment (Back Raster)

1) Remove the video signal

2) Adjust the sub-brightness of back raster to be 0.85FT±0.15FT with SUB BRIGHTNESS volume VR501.

3) And, adjust the color temperature to be X=0.281 ±0.015 and Y= 0.311 ±0.015 by R.G.B bias control function on OSD menu.

4) Adjust BRIGHTNESS to be 0.85FT ±0.15 FT.

White Balance adjustment (Video)

1) Input the 25% window pattern with 31KHz 640*480 mode.

2) Adjust the color temperature to be X=0.281 ±0.015 and Y=0.311 ±0.015 by R.G.B gain on OSD menu.

3) Adjust CONTRAST to be 60FT ±5 FT.

7-3. 6. Purity and Convergence Adjustment.

1) Purity Adjustment.

①Demagnetize the picture tube and cabinet using a degaussing coil.

②Turn the CONTRAST and BRIGHTNESS controls to maximum.

③Adjust RED and BLUE bias controls to provide only a green raster

④Loosen the clamp screw holding the yoke, and side the yoke, backward to provide vertical green belt(zone) in the picture screen.

⑤Remote the Rubber wedges.

⑥Rotate and spread the tabs of the purity magnet see figure 1 around the neck of the picture tube until the green belt is in the center of the screen. At the same time, center the raster vertically.

⑦Move the yoke slowly forward until a uniform green screen is obtained. Tighten the clamp screw of the yoke temporarily.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 20/30 |

⑧Check the purity of the red and blue raster by adjusting the bias controls.

⑨Obtain a while raster, referring to "CRT GRAY SCALE ADJUSTMENT

⑩Proceed with convergence adjustment.

2) Convergence adjustment.

①.Receive crosshatch pattern with a color bar signal generator.

②.Adjust the BRIGHTNESS and CONTRAST Controls for well defined pattern.

③.Adjust two tabs of the 4-Pole Magnets to change the angle between them(See figure 1) and superimpose red and blue vertical lines in the center area of the picture screen.

④.Turn both tabs at the same time keeping their angles constant to superimpose red and blue horizontal lines at the center of the screen.(See figure 2.)

⑤.Adjust two tabs of 6-Pole Magnets to superimpose red/blue line with green one. Adjusting the angle affects the vertical lines and rotating both magnets affects the horizontal lines

⑥.Repeat adjustment 3,4,5 Keeping in mind red, green and blue movement, because 4-Pole Magnets and 6-Pole Magnets interact and make dot movement complex.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 21/30 |

8. DESCRIPTION OF CIRCUIT OPERATION

8-1. Mode control

8-1.1. H-Sync is inputted to pin 30 of IC601, V-Sync to pin 29 of IC601 for each mode, and pin 27, 26 of IC601 output always-positive polarity sync.

8-1.2. The outputs from IC601 are as below (See Table 1)

| No. | Frequency | Resolution | Range of Frequency | OUT PUT (MCU PIN) |
| --- | --- | --- | --- | --- |
|  | Hf KHz | Vf Hz |  | Hf (kHz) | Vf (Hz) | CS3 38 | CS2 39 | CS1 40 | SUS- 4 |
| 1 | 31 | 70 | 720x400 | 28∼32.9 | 68∼72 | L | L | L | H |
| 2 | 31 | 60 | 640x480 | " | 58∼62 | L | L | L | H |
| 3 | 35 | 86 | 1024x768 | 33∼35.9 | 84∼88 | H | L | L | H |
| 4 | 38 | 75 | 640x480 | 36∼40.9 | 73∼77 | H | H | L | H |
| 5 | 38 | 60 | 800x600 | 36∼40.9 | 58∼62 | H | H | L | H |
| 6 | 47 | 75 | 800x600 | 41∼51.9 | 73∼77 | H | L | H | H |
| 7 | 48 | 72 | 800x600 | " | 70∼74 | H | L | H | H |
| 8 | 48 | 60 | 1024x768 | " | 58∼62 | H | L | H | H |
| 9 | 53 | 85 | 800x600 | 52∼61.9 | 83∼87 | L | H | H | H |
| 10 | 56 | 70 | 1024x768 | " | 68∼72 | L | H | H | H |
| 11 | 60 | 75 | 1024x768 | " | 73∼77 | L | H | H | H |
| 12 | 64 | 60 | 1280x1024 | 62∼70 | 58∼62 | H | H | H | H |
| 13 | 69 | 85 | 1024x768 | 62∼70 | 83∼87 | H | H | H | H |
| 14 | - | - | - | H≤10 | NORMAL | X | X | X | L |
| 15 | - | - | - | NORMAL | V≤40 | X | X | X | L |
| 16 | - | - | - | H≤10 | V≤40 | X | X | X | L |
| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 22/30 |

8-2. Deflection Processor (IC301)

8-2.1. Horizontal section

1) Horizontal oscillation

R314 and C347 set horizontal free frequency to 48KHz.

Auto-sync processing can be done from 30KHz to 70KHz by mean of IC301 without any adjustment.

2) Phase shift

Horizontal phase shift is controlled by IC601 using I2C BUS control.

3) Horizontal driver output

The output pulse, which has the duty-cycle of 47%, is available at pin 26 of IC301.

This output is used for horizontal drive circuit.

4) B+ control driver output

The output pulse is available at pin 6 of IC301 and it is used for

H-scan voltage control driver.

5) X-ray protection

When the fly-back voltage rises up to unacceptable level X-ray protection is activated X-ray input pin 13 of IC601 is above 4V.

This result is that the completed line drive stage stops working.

The reset of this protection is obtained by Main power off.

8-2.2. Vertical section

1) Vertical oscillation

The free running frequency of the vertical oscillator is determined by the capacitor C342 at pin VCAP (pin22) of IC301.

2) Vertical amplitude

Vertical amplitude is controlled by IC601 using I2C.

3) Vertical position

Vertical position is controlled by IC601 using I2C.

4) Ease-west parabola

A parabola waveform is available on pin 24 of IC301 for driving the pincushion correction stage. Amplitude of parabola waveform is controlled by IC601 using I2C.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 23/30 |

8-2.3. B+ Regulator

B+ PWM regulator output is available on pin 28 of IC301 for driving the B+ control stage. This PWM output is adjusted through VR301.

8-3. Vertical Deflection (IC201)

IC201 (KA2142) is used for direct driving of vertical deflection yoke.

8-4. Horizontal scan voltage control stage

The step-up converter is used in this stage.

The output pulse at pin 28 of the IC301 is synchronized on horizontal frequency. And this pulse is operated via buffer stage Q311/Q312.

This output is rectified through D315/L304.

In this way, the supply voltage to the fly-back transformer can be proportional to the horizontal line frequency.

8-5. Horizontal deflection output stage

8-5.1. Line driver stage

As a driver device, small MOSFET Q307 (IRF630) is used.

The driver transformer T302 is equipped with a snubber circuit (R327/C309) at the primary side to damp excessive ringing.

8-5.2. Horizontal power output stage

The horizontal power output stage is a conventional one with a diode modulator.

As a deflection transistor, the Q308 (2SC5682) is used.

To compensate the horizontal linearity, T301 is connected in a series

with the horizontal DY. It is controlled by DC collector voltage of Q304,

which the base voltage of Q304 is integrated from output at pin 22 of

IC601.

8-5.3. S-correction capacitor switches

Q316 is off when horizontal frequency is 35KHz.

Q316, Q317 is off when horizontal frequency is 37KHz.

Q316, Q318 is off when horizontal frequency is 43KHz-52KHz.

Q317, Q318 is off when horizontal frequency is 53KHz∼61KHz.

Q316, Q317,Q318 is off when horizontal frequency is 62KHz∼70KHz.

Q316, Q318 is off when input is override condition.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 24/30 |

8-6. FBT (Fly-back Transformer)

The high voltage for CRT anode focus, G2 voltage for CRT and - 12V for vertical deflection are generated by the FBT.

Also, -130V for G1 voltage, -12V for the vertical supply voltage are extracted from the FBT.

8-7 ABL (Automatic Beam Limiting)

The voltage of the FBT pin10 is affected by the anode current of the FBT.

When the voltage at pin 10 is decreased, the anode current is increased accordingly. When the current anode is increased, contrast is set at the certain limited level (28FL in white pattern) that is set by inner voltage of IC401.

8-8. Video amplification section.

8-8.1. Video pre-amplifier (IC401)

Input video signals are amplified by means of IC401, and the amplified signals drive the video output stage (IC402).

Video gain is adjusted by DC voltage at pin 12 for ABL control.

8-8.2. Video output stage (IC402)

The video output signal from IC401 is amplified again by IC402, and IC402 apply video signal to each cathode of CRT.

Q405, Q406 and Q407, which is operated by I2C BUS control through u-com, adjust cutoff voltages.

8-8.3. OSD (On Screen Display: IC403)

The OSD signal is applied from IC403 to IC402.

It is controlled by I2C BUS control line.

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 25/30 |

9. TROUBLE SHOOTING

9-1. NO POWER

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 26/30 |

9-2. NO VIDEO

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 27/30 |

9-3. NO RASTER

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 28/30 |

9-4. TROUBLE IN HORIZONTAL SIZE

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 29/30 |

9-5. TROUBLE IN CONTRAST

| TOVIS | TOVIS P/N | MTG-1972XN | DATE | 2002.03.11 |
| --- | --- | --- | --- | --- |
|  |  | Color Monitor Service Manual | REV NO. | 0 |
|  |  |  | PAGE | 30/30 |

9-6. TROUBLE IN BRIGHTNESS

# Text boxes

CHECK C101

AC LEVEL

min->1-99->max

NO POWER

CHECK&

REPLACEMENT

F101, POWER CORD, F101

CHECK & REPLACEMENT

BD101

CHECK & REPLACEMENT

IC101

CHECK C104

DC LEVEL

CHECK IC101

#1 WAVEFORM

CHECK &

REPLACEMENT

SECONDARY VOLTAGE OF T101

NO

YES

YES

YES

NO

NO

CHECK

SIGNAL CABLE

CHECK&

REPLACEMENT

SIGNAL CABLE

NO

YES

NO VIDEO

CHECK IC401

#21,24,26 PULSE

CHECK IC401

#23 DC LEVEL &

#18,19 PULSE

NO

NO

CHECK&

REPLACEMENT

IC601, Q204

YES

CHECK IC402

#1,3,5 PULSE

CHECK&

REPLACEMENT

IC402

NO

CHECK&

REPLACEMENT

CRT SOCKET, G1

YES

NO RASTER

YES

CHECK & REPLACEMENT

Q113, Q307, D315

CHECK

HV & G2

CHECK Q308

WAVEFORM

CHECK

G1 & DC 80V

CHECK L304

DC 55V

CHECK & REPLACEMENT

D110

CHECK & REPLACEMENT

Q507, Q508, Q509

NO

YES

NO

NO

CHECK&

REPLACEMENT

IC401

YES

CHECK & REPLACEMENT

FBT, CRT

YES

NO

YES

H-SIZE

CHECK IC301

#24 WAVEFORM

CHECK Q309

COLLECTOR

WAVEFORM

CHECK IC601

#19 WAVEFORM

CHECK & REPLACEMENT

IC601

YES

NO

YES

YES

NO

NO

CHECK & REPLACEMENT

Q309

CHECK & REPLACEMENT

IC301

CHECK & REPLACEMENT

IC302

CHECK & REPLACEMENT

IC601

NO

NO

CHECK & REPLACEMENT

IC401, R518, ZD501

CHECK IC401

#12 VOLTAGE

CHECK IC401

#18 WAVEFORM

CONTRAST

YES

CHECK & REPLACEMENT

IC401

YES

YES

CHECK & REPLACEMENT

Q507, Q508

YES

CHECK C504

VOLTAGE

CHECK & REPLACEMENT

R520, D506

NO

NO

CHECK & REPLACEMENT

Q202

CHECK

G1 VOLTAGE

BRIGHTNESS

Color Monitor Service Manual

MODEL: MTG – 1972XN

(FOR IGT AUSTRALIA)

1

19