# Text boxes

###### ITHACA MODEL 850 TICKET PRINTERS

SENSORS & SWITCHES

#### Open/Close Sensor

Located on communication board. In rear of outer chassis.

Determines if the Printer inner chassis is racked out (open)

See FIG 2.

#### Paper low Sensor

Optically senses the tickets in ticket tray. Senses 30-35 tickets remaining in ticket tray. Reports paper low to game in the status byte. Verify with Game manufacturer how status byte is managed. See FIG 1.

#### Top of Form Sensor

Senses black dot on right edge of ticket. See FIG 1.

#### Ticket Taken Sensor

Used to determine when customer has removed the printed ticket. See FIG 1.

#### Head-Up Switch

Signals when thermal printhead assembly has been opened.

Located under the printhead, not visible from the top of printer

#### Ticket  Feed Switch

Located on controller board operated by Feed Button.

See FIG 3.

# Stand-Alone

## Print Test Ticket

REMOVE POWER

IGT – Power down the game.

WMS - external power supply

Rack out printer assy.

Block open /close position sensor.

( RS232  printer ) See FIG 2.

Hold down ticket feed button. See FIG 3.

Apply power.

Ticket prints.

IGT 10 pin

WMS 14 pin

### Printer Status LED

The printer has been outfitted with a LED indicator system that provides the condition of the printer by using a series of blinks to communicate the status of the printer. If a customer supplied Bezel is installed, the status of the Bezel will be identical to the LED

The following table lists the different LED indications and provides a brief description.

| Condition | Status LED/Bezel |
| --- | --- |
| Unit Ready | On |
| Head Up | Med Blink |
| Door Open | Med Blink |
| Paper Out | Slow Blink |
| Temperature Error | Fast Blink |
| Paper Jam | 4 Blinks Pause |
| Ram Error | 2 Blinks Pause |
| Checksum Error | 5 Blinks Pause |

TROUBLESHOOTING

Error on IGT game screen

“Wrong type of paper” and printer buzzer beeping. This is caused by the ticket perforation not breaking  as the customer takes ticket pulling the leading edge of the next ticket passed the top form and under the ticket taken sensor.

To clear error reload ticket.

Ticket won’t load on IGT game

Printer will have to power cycled or the game rebooted.

To clear error  Reboot the game.

Gray 30 pin flex cable getting pinched. Care has to taken when closing the inner slide assy.

CAUTION never unplug the gray 30 pin flex cable with the power on. Damage to the communication board will result.

Gray 30 pin flex cable

##### Two different interfaces are used in 850 printers

##### IGT Netplex

Communication board # E030062-01 (10 pin connector on communication board )

Powered through a 8 pin pigtail connector

Controller board Firmware PE88xx

All Other Game Manufacturers  RS232 Serial

Communication board # 85-03526 (14 pin connector on communication board )

Powered through a external power supply

Controller board Firmware PP85xx

Ticket Taken Sensor

TOF

POSITION OF TICKET AT TOP OF FORM

LOOKING DOWN ON PRINT MECH

ticket

TOF

Lead edge of ticket should be positioned as shown in  cutout of platen cover

TTS

Communication Brd

FIG 1

FIG 2

FIG 3