Bally EVO and EVO Hybrid

What makes a Bally EVO Hybrid different from a regular Bally EVO?

Reel mechanisms and control board have been added.

What options and operations are set by DIP Switches on the Bally EVO?

Autoplay

Ignore Checksum

Show State Status

Host Override

Printer / Hopper Override

Watchdog Override

EEPROM Clear

SafeRAM Clear

Deluxe Sound Enable

Enable 12-button deck

Bill to Tray Option

Touchscreen Enable

Progressive change enable

Show Error Log

What options and operations are controlled by jumpers on the Bally EVO?

Battery Enable

Where does the SafeRAM Clear chip go on the MPU board on the Bally EVO?

U78

Should you were a grounded anti-static wrist strap when changing an EPROM?

Yes

What Jurisdiction Code (or Market Code) do we use on a Bally EVO game after clearing SafeRAM?

5

What options must be set up in software after doing a SafeRAM Clear on the Bally EVO?

Jurisdiction

Chassis Type

Coin Acceptor type

Bill Acceptor type

Hopper type

Door type

SAS Version

EFT (Electronic Funds Transfer)

Secondary device

Touchscreen calibration

Denomination setting

Maximum / Minimum bet

Game specific options

How do you measure the battery voltage on the Bally EVO without gaining access to the MPU board?

SafeRAM test

How do you find the SMI Number for the game without gaining access to the MPU board on the Bally EVO?

Diagnostics Mode

How are the General Purpose I/O operations for a Bally EVO structured?

A.	Serial

B.	Paralle <<<<<<<l

C.	Matrix

How do you activate an Output in Output Test on the Bally EVO?

Touch the screen or select with the buttons.

On the Bally EVO when you activate an out the color changes to show that that output actually changed state. (T/F)

False. The change shows what it should be but the MPT has no way of knowing that the output actually went high or low.

What loopback jumpers are required to test the Serial I/O Ports on the Bally EVO?

What test would you use on the Bally EVO to confirm that the reel mechanisms are mechanically working properly on the Bally EVO?

Reel test

What test would you use to adjust reel positions on the Bally EVO?

Reel Calibration test

What test would you use on the Bally EVO to confirm the reel symbols match the symbols on the monitor?

Reel Strip Test

What test would you use to print a test ticket on the Bally EVO?

Printer Test in Diagnostics

What configuration options are set by the Configuration menu on the Bally EVO?

Out of Service mode

Turn games on or off

Date / Time

Hopper and credit limits

Coin denomination (view but not change)

Tower operations

Progressive setup

Terminal ID

Max Bet options

Casino Location

Which tower Lamp configuration do we use?

0

What signals do we have on a CC-16 12V Inhibit Coin Comparator?

+12 VDC

Ground

Sense Output

Inhibit Input

What signals do we have on a CC-62 Coin Comparator?

+12 VDC

Ground

Sense Output

Inhibit Input

Error Output

Credit Output

On a CC-62 what is the difference between the Sense Output and the Credit Output?

Sense indicates that a good coin was detected by the Accept coil.

Credit indicates that the coin was sensed going in the proper direction.

What makes the MC-xx series of Coin Comparators different from the CC-xx series?

The CC-xx series have all analog electronics. The MC-xx series are microcontroller based.

On an MC-xx Coin Comparator what does it mean when the LED is RED?

Tilt of some kind, stuck coin, reverse coiin detected, the comparator didn't pass its own self test for some reason.

What signal names would you expect to find on an RS-232 port?

(minimal)

Ground

Rx (receive Data, Serial Data In)

Tx (Transmit Data, Serial Data Out)

(optional)

RTS (Request to Send)

CTS (Clear to Send)

DTR (Data Terminal Ready)

What voltage does the Player Panel Lamps run on on a Bally EVO game?

7.5 VAC

What color are the ground wires for low power circuits iin general on a Bally EVO?

Gray with an Orange stripe or just Gray

How does the Touch Screen communicate to the MPU on a Bally EVO?

Serial I/O port

How does the Seiko Ticket Printer communicate with the MPU on a Bally EVO?

Serial I/O port

What power does the Seiko Ticket Printer run off of on a Bally EVO?

24 V DC

What voltage does the Touch Screen Controller run off of on a Bally EVO?

12 VDC

On a Bally EVO game where does the Coin Comparator get its power?

Coin-In Optics Assembly

What are the signal names on the Coin-In Optics assembly of a Bally EVO?

+24 V

+5 V

Reset

Credit

Error

Coin Sense

Coin Comparator power (24 VDC)

When doing troubleshooting a Bally Coin-In Optics Assembly you can't get the "A" optic to work. Is this normal?

Yes. The Coin-In Optic Assembly must get a Sense signal from the Coin Comparator before the "A" optic is enabled.

What voltage does the Coin Diverter (Deflector) get its power from on a Bally EVO?

24 VDC

On a Bally EVO using an XS-1200 hopper what signal names would we find on the hopper connector?

Printer / Hopper jumper wire

Reset

Fill Switch

Door Switch

Forward Sense

Forward Enable

Forward / Reverse Control line

reverse Enable

Coin Out

Coin Probe

24 V

Ground

On a Bally EVO what color are the wires for the +24 V DC line?

Yellow wire with a Blue Stripe

On a Bally EVO what voltage do we have coming out of the power supply modules?

+3.3 V

+5 V

+12 V

+5V SB

-12 V

-5 V

Ground

+24 VDC

7.5 VAC

19 VAC

On a Bally EVO game what voltages do the reels run off of?

24 VDC

What voltages and signals are on the Tower Lamp?

7.5 VAC and active low lamp enable lines.

If an output is driven by a Low Side Driver (low when that output should be enabled) we can troubleshoot that output by pulling it to ground and seeing if the output works. Like a Tower Lamp or Diverter, we can light the lamp by pulling the signal to ground. (T/F)

True, use the right ground line.

On Bally games most cable assemblies start with what as their part number?

"CBL-"

On Bally games most mechanical Assemblies start with what as their part number?

"AS-"

On Bally games most electronics assemblies start with what as their part number?

"E-"

On Bally games most Circuit Boards start with what as their part number?

"AS-003356-xxx"

Bally games use a one-board Coin-In Optics Assembly. How do the Optics work with only one board?

The light is bounced back to the board by a prism.

What type of processor is used on the Bally EVO?

Two. The MPU uses an MC68332. A IBM PC type, Pentium 3, is used for graphics.

What voltage does the cabinet fan run on in a Bally EVO game?

120 VAC

What voltage does the fluorescent lamps run on in a Bally EVO?

120 VAC

What model numbers are considered to be Bally EVO?

V8700

What model numbers are considered to be Bally EVO Hybrid?

On a Bally game what type of lamps are used in the Tower?

#159, 6.3 V, T3 1/4, wedge base

On a Bally game what type of lamps are used in the Player Panel?

#86, 6.3 V, T1 3/4, wedge base