Bally V7200

What is the difference between a Bally V7214, V7217 and V7219?

All are video games, V7214 is 14" screen, V7217 is 17", V7219 is 19". Same basic MPU and power supply, etc.

How many V7200 games can you put on a 20 Amp service?

6

On a Bally V7200 game how do you set the game up so that the Bet Max button repeats the last bet made?

DIP switch 1, section 1, On

On a Bally V7200 game how do you set the game to ignore a Checksum failure on Self test?

DIP switch 1, section 2, On

On a Bally V7200 game how do you set "Show State Status" active?

DIP switch 1, section 3, On

On a Bally V7200 game how do you set "Host Override" active?

DIP switch 1, section 4, On

On a Bally V7200 game how do you set "Printer / Hopper Override" active?

DIP switch 1, section 5, On

On a Bally V7200 game how do you inhibit the Watchdog timer operation?

DIP switch 1, section 6, On

On a Bally V7200 game how do you enable clearing the EEPROM during SafeRAM?

DIP switch 1, section 7, On

On a Bally V7200 game how do you enable SafeRAM?

DIP switch 1, section 8, On. Insert SafeRAM EPROM.

On a Bally V7200 game how do you enable the Deluxe Sound Board?

DIP switch 2, section 2, On

On a Bally V7200 game how do you enable the 12 button player panel?

DIP switch 2, section 4, On

On a Bally V7200 game how do you enable the "Bill to Tray" feature?

DIP switch 2, section 5, On

On a Bally V7200 game how do you enable the Touch Screen?

DIP switch 2, section 6, Off

On a Bally V7200 game how do you enable changing the Progressive values during SafeRAM?

DIP switch 2, section 7, On

On a Bally V7200 game how do you get the error Log to be displayed?

DIP switch 2, section 8, On

On the Bally V7200 series games what jumper do you have to change if you are upgrading EPROMs to a version higher than 12?

W19 in (4 MB EPROM size)

When installing a new logic board which jumper do you have to move to enable the Battery?

W17

How do you do a SafeRAM on a Bally V7200 game?

Insert SafeRAM Clear chip V7S1000CLEAR-02 in socket p10 and set DIP switch 1, section 8 to On. Power up. Turn audit Key.

Do SafeRAM.

Remove board. Turn DIP switch off. Replace SafeRAM Cear chip. Reinstall board.

Set EEPROM options.

Calibrate Touchscreen

How do you set Jurisdiction (Market Code) on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you set SAS Host Address on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you set Chassis type on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you set Coin Comparator type on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you set Bill Acceptor type on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you set Ticket Printer type on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you set Hopper type on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you set Door type on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you enable the Double Down feature on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you enable Tournament mode on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you enable the EFT (Electronic Funds Transfer feature on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

How do you set Jurisdiction (Market Code) on a Bally V7200 game?

Do SafeRAM. Set up EEPROM options.

On a nickel game that plays bets in pennies it is possible to credits left on the game representing pennies that can not be cashed out of the hopper. How do you tell the game to Hand Pay the credits or play them off?

Do SafeRAM. Set up EEPROM options. Residual Credits Mode.

If the touchscreen is not functioning properly and will not calibrate will doing a SafeRAM help?

No, in fact it's a bad idea to do a SafeRAM if the touchscreen is not working. After SafeRAM the game automatically does a touchscreen calibration. If it won't calibrate you can't finish the SafeRAM procedure and Setup options. if you find yourself in this position set the DIP switch to disable the touchscreen and redo SafeRAM.

How do you set currency type on a Bally V7200 game?

After SafeRAM

How do you prevent the hardmeters from incrementing when you do the Output test?

Press "Lock Meters" on the screen

In output test on a V7200 game the outputs on the screen will change colors when that output is activated. Does the change of color show that the output actually went high or low?

No. It only indicates what the output should be doing. The game has no way of knowing if the output actually went high or low.

What test would you use to test the Coin Acceptor on a Bally V7200 game?

Diagnostics Menu. Coin / Bill Acceptor test. Insert bill or coin.

How would you check for an intermittent thermal problem in System RAM?

Diagnostics Menu. Memory Test, System RAM test. Subject the RAM chips to thermal stress with a heat gun and freeze spray.

Why do we have two Main EPROM chips?

M0 and M1 are both 8-bit wide memories. The processor is a 16-bit machine. M0 has low byte information. m1 has High byte information.

What type of processor is used in a Bally V7200 game?