TOP OF FORM SENSOR (TOF) CALIBRATION

## WHAT IS SENSOR CALIBRATION

Electronically the TOF sensor circuit is set up or calibrated to differentiate between the white ticket paper and the preprinted black TOF mark.

## WHEN DO YOU CALIBRATE

Installing a new   control board

Changing the  TOF sensor

Changing the Firmware chip

HOW IS CALIBRATION DONE

Calibration will automatically be done as soon as power is supplied to the printer.

# IMPORTANT

For the calibration to be done properly, the sensor has to be looking at white paper.

PROCEDURE

Manually load a ticket so white paper is under the TOF sensor and close the platen cover.

Apply power to the printer.

The printer will beep in a few seconds indicating the calibration was done.

HOW DO I RECALIBRATE

Lets say you applied power and forgot to have the TOF sensor looking at white paper.

YOU’RE SCREWED

Not really, if you have access to a different firmware chip (different part number )

EXAMPLE You have a PP8505 WMS chip in the printer that needs to be calibrated.and have an IGT game which has a PE8802 chip in it. Take the chip from the IGT printer install it in the WMS printer and recalibrate. Now put the WMS PP8505 chip back in the printer and recalibrate again. When you reinstall the IGT printers chip make sure you have the ticket loaded with white paper under the sensor.

Note: May 17, 2006 – At TechFest 13, Transact announced that they now have a TOF calibration IC that pops into the unit so you don’t have to seek out a different revision firmware in order to “trick” it into recalibrating. No part number. Contact Transact and ask for a TOF Reset chip.

Sending the command [gs]<0x7f><7> thru the Pjterminal program will also calibrate without changing chips.