www.jcm-american.com

##### PRODUCT PROFILE

925 PILOT ROAD  (  LAS VEGAS  (  NEVADA 89119  (  702-651-0000  (  FAX 702-651-9912

UBA™ BILL VALIDATOR

The UBA™ bill validator builds on JCM’s world-famous world bill acceptor (WBA), with improved bill-sensing technology and lightweight, durable plastic construction. This one unit can accept all of the world’s currency up to 85mm in width without any hardware changes and can hold up to 500 notes. The UBA comes complete with the latest sensing technology, utilizing magnetic and optical sensors. Infrared, red and green LEDs, phototransistors, UV, reflective, transparency and bar code sensors comprise the UBA’s optical sensing package. The UBA also features forward and backward compatible cash boxes for seamless integration onto your slot floor.

Convenience

- Automatic centering mechanism centers notes in the middle of the bill path regardless of how the bill was inserted. This allows for a greater first time acceptance rate because the bill is directly in the middle of the head when it is scanned. Centering also eliminates the need for additional bill guides in the entry bezel and cash box.

- The automatic retry feature will re-scan a bill up to three times before rejecting. This greatly increases the acceptance rate.

- The USB download port is located in the front of the unit for easy accessibility. It allows for quick and easy program downloads without having to remove the unit from the game.

- Communication between the game and the validator can be achieved through the USB port in the rear of the unit, or the same standard connection as the current WBA can be used.

- Plastic cash box is manufactured from a high impact, highly durable plastic that resists damage and is backward compatible with all WBA units that are currently in the field. There is also a viewing window that allows the last bill stacked to be seen without having to open the cash box.

- The UBA is the same size as the current WBA and mounts in the same fashion. The front bezel mounting configuration remains the same as the WBA as well.

Security

- The anti-pullback roller device prevents “stringing.” The device has interlocking teeth that eliminates the ability for somebody to pull a bill back through the entry.

Sensing

- Improved sensing technology makes use of magnetic and optical sensors to validate the currency.

- Optical sensing consisting of infrared, red and green LEDs, phototransistors, UV, reflective, transparency and bar code sensors.

- Accepts currency from multiple countries at the same time without having to change validator software.

# # #

Contact: Michele Crawford, JCM				Paul Speirs, Steinbeck Communications

(702) 651-0000				(702) 413-4278